## Slide 1
DATASHEET
HAMBURG 650W

## Slide 2
Fully compatible with Intel ATX 3.1 specifications.
80 PLUS® 230V EU certified, deliver great efficiency under real world condition.
Low-profile etched flat cables.
High quality 105°C/221°F main capacitor.
650W continuous output at 40°C/104°F operating environment.
Ultra-quiet 120mm cooling fan delivers excellent airflow at an exceptionally low noise level.
High amperage single +12V rail design.
DC-DC design for more precise electrical output.
Intel C6/C7 states & ErP ready
Built-in industry grade protections: OCP, OVP, UVP, OPP, SCP, OTP.
Compact Sizing: 150mm(W)x86mm(H)x140mm(D).
3 years warranty.
Features
HAMBURG 650W

## Slide 3
Supports 200% power excursion
Reaches 60% low load efficiency
Complies with required power supply timing standards
Fully Compatible With ATX 3.1 Specifications
Meets all the needs of a computer system, providing powerful and stable power.
Highlighted Features
Low-Profile Flat Black Cables
Makes cable management easier.
High Amperage Single +12V Rail & DC to DC Design
Powerful single +12V rail and DC to DC design for the best compatibility.
High Quality 105°C/221°F Main Capacitors
Improves the durability and offers the highest stability and reliability.

## Slide 4
Supports Energy Star 5.0* energy standard
Thermaltake GERMAN series is suitable for use in Energy Star-compatible computers.
Supports Intel Deep Power Down C6/C7 Status
Helps your PC system operate more power efficiently.
Corresponds to the EU directives on WEEE and RoHS
Thermaltake considers its full impact on the environment during manufacturing and maintains green facilities to ensure Thermaltake GERMAN series meets WEEE & RoHS requirements.
80 PLUS® 230V EU Certified Efficiency
Delivers top end efficiency under real world load conditions.
Eco Design

## Slide 5
GENERAL INFO | 
P/N | W0650RE
Model | TR3S-650AH2NLW
Max. Output Capacity | 650W
Dimension | 150mm(W)x86mm(H)x140mm(D)
PFC | Active PFC
Power Good Signal | 100-150 msec
Hold-Up Time | > 17msec at 80% load
Cooling System | 12cm FDB Fan
ENVIRONMENT | 
Operating Temperature | 5°C to + 40°C
Operating Humidity | 20% to 85%,non-condensing
Storage Temperature | -40°C to + 55°C
Storage Humidity | 10% to 95%, non-condensing
MISCELLANEOUS | 
Efficiency | 80 PLUS® 230V EU Certified.
MTBF | 100,000 hrs minimum
Safety Approval | CB/CE/TUV/LVD/UKCA/RCM
Protection | OCP/OVP/UVP/OPP/OTP/SCP
PCIe CONNECTOR | 
PCIe 6+2pin | 2
Specification
AC Input | Input Voltage: 200-240V～ |  |  |  | 
 | Input Current: 6A |  |  |  | 
 | Frequency: 50Hz/60Hz |  |  |  | 
DC Output | +3.3V | +5V | +12V | -12V | +5VSB
Max Output Current | 18A | 18A | 54.2A | 0.3A | 3A
Max Output Power | 110W |  | 650W | 3.6W | 15W
Total Power | 650W |  |  |  | 

## Slide 6
Connector and Cable Specification
PCIe
(6+2Pin)
X 1
500mm+150mm
X 2
Connector
Type
Connector
Quantity
Cable
Quantity
Cable
Length
Peripheral
(4Pin)
X 1
500mm+150mm
+150mm+150mm
X 4
SATA
(5Pin)
X 1
500mm+150mm
+150mm+150mm
X 4
X 1
ATX 12V
(4+4Pin)
650mm+150mm
X 2
X 1
Main Power
(24Pin)
600mm
X 1

## Slide 7
Total Protection
Protections | Voltage Source |  | 
 | +3.3V | +5V | +12V
Over Voltage Protection | 3.76~4.3V | 5.74~7.0V | 13.4~15.6V
Under Voltage Protection | 2.0~2.6V | 3.3~3.9V | 8.5~9.7V
Over Current Protection | 25~40A | 25~40A | 93~117A
Over Power Protection | Protection at 160%~200% over peak load. |  | 
Over Temperature Protection | Protection temperature is 45℃~55℃ |  | 
Short Circuit Protection | Short circuit placed on +5V,+12V,+3.3V,-12Vwill latch off. +5VSB will auto-recovery. |  |